## Slide 1: Progress4: Scalable Multi-FPGA Runtime
Direct PCIe Access
Host
FPGA A
Registers
Memory
PCIe
FPGA B
Registers
Memory
PCIe
FPGA C
Registers
Memory
PCIe
Separate Host connection per FPGA
Limited by Host PCIe connectivity
Fabric-Based Access
Host
Ref FPGA
Registers
Memory
PCIe
Fabric
FPGA B
Registers
Memory
Fabric
FPGA C
Registers
Memory
One Host entry via Ref
Unified register and memory access
Extend through inter-FPGA links
9
Notes: Runtime operations such as global pause and state management require Host access to each FPGA's registers and memory. The baseline dual-board prototype uses a separate PCIe connection to each FPGA. Fabric provides a shared Host entry through the Ref node and carries resource requests over inter-FPGA links. Ref also retains its local DUT and resources. The diagrams illustrate architecture; three nodes and chain links do not claim a validated three-FPGA deployment. Access bandwidth is shared at Ref, and supported scale still depends on links and implementation constraints. Fabric components and the Driver backend are implemented; the dual-node Cosim environment is established. Current documented evidence does not establish complete end-to-end or Fabric board-level validation. At the user's request, these status lines and the illustrative-topology caption are omitted from the visible slide, not converted into success claims. Sources: src/midterm/progress/runtime.tex; ../docs/source/project-notes/fabric/status.md. Design reference: figure/presentation-reference/midterm-runtime-09-v1.png. All visible text, diagrams, and arrows are native editable PowerPoint elements.