## Slide 1
Distributed FPGA State
Global Snapshot on Host
Restore / Replay Paths
FPGA 0
Partition 0
Partial DUT RTL
Registers
SRAM
Combinational Logic
DDR 0
Scan Chain
Data
(part 0)
RAM Model
Data
FPGA 1
Partition 1
Partial DUT RTL
Registers
SRAM
Combinational Logic
DDR 1
Scan Chain
Data
(part 1)
...
Dashed boundary: scanned state
ckpt/
DUT Cycle 100 ...
DUT Cycle 20
0/ · DUT Cycle 0
scanchain
part_0
scanchain
part_1
RAM Model
Data
All partitions · same cycle
Input Traces
State Mapping
Metadata
Supporting records and metadata
FPGA Restore
FPGA
Write back by partition
Restore local states
Software RTL Replay
Decode by state mapping
Restore and replay
Notes: Standalone thesis figure rebuilt from figure/ckpt-and-replay.png. Dashed partition boundaries include registers and SRAM, not combinational logic. Host collects all partition data for the same DUT cycle. Only illustrative cycle 0 is expanded; cycles 20 and 100 are compact overlapping cards. Input Traces are supporting records for hardware/software restoration and replay; their dependencies are described in the report rather than drawn as extra arrows. State mapping metadata is used to decode partition state for software RTL replay. The three-chip stack indicates multiple FPGA targets, not a measured platform size. File labels are conceptual, not a complete on-disk schema.