## Slide 1: 8. Automated Multi-FPGA Circuit Partitioning
Automated Partitioning
1
Adaptive-granularity
RTL partitioning
2
KaHyPar-based
hypergraph partitioning
3
Path-cut analysis
for LI-TDM
Preliminary observation
Smaller graphs and faster solving
on well-structured RTL.
Post-Synthesis Resource Utilization
KMH · Two partitions · Utilization (%)
Chart: 
| LUT | FF | BRAM
Part 0 | 73.18 | 17.66 | 14.31
Part 1 | 75.77 | 8.17 | 0
Similar LUT usage, uneven FF and BRAM distribution.
EMU_SYSTEM synthesis; percentages of device capacity.
8
Notes: REMUS implements adaptive RTL granularity selection, weighted hypergraph partitioning using KaHyPar, and path-cut analysis for LI-TDM configuration. The author reports preliminary observations on well-structured hierarchical designs: graph size around one tenth and hypergraph solver time around one seventh of the netlist-level baseline, with similar Cut Size, scalar balance and Path-Cut Number. The baseline runs are not finished. These ratios are NOT finalized results and are omitted from the slide. Confirm matched DUTs, configurations, graph-size definition and timing boundaries before publishing quantitative gains. Solver time is not total transformation time. The main chart uses archived KMH two-Part Vivado 2024.2 synthesis results: Part 0 LUT/FF/BRAM utilization 73.18/17.66/14.31 percent; Part 1 75.77/8.17/0.00 percent. BRAM counts are 288.5 and 0 tiles. URAM is 13 versus 0, omitted from the plot for focus. The scope is role_i/ClockResetCore_0/emu_system, including inserted infrastructure; not pure DUT, full board consumption, or post-route utilization. The denominator is whole-device capacity, not the remaining Part budget. The observed resource asymmetry does not isolate adaptive granularity or scalar weights as its sole cause. Constraints, module grouping and synthesis mapping may also matter. Exact build matching between partition summaries and synthesis reports remains to be completed, so no estimation-error or baseline-gain inference is made from their combination. This motivates the resource-modeling discussion and proposed multidimensional constraints on slide 11, without asserting that the planned improvement is already proven. Sources: experiments/synthesis-utilization.md (3.2); src/midterm/progress/partitioning.tex; src/midterm/problems.tex.